## Slide 1
Arduino
25cm
20cm
GND
+ 5V
OUT 1
OUT 2
OUT 1
OUT 1
OUT 1
OUT 2
OUT 2
OUT 2
LEGEND:
Red line: Layer 1 (connections)
Black line: Layer 2: Power
+: Coil positive terminal
-: Coil negative terminal
Out1/2: Outputs to coils
Parts are to scale.

## Slide 2: Parts
DPDT GDAK:
ULN2803A:
DC Jack RAPC 722x
Part | Source
16x DPDT Relay Omron G6AK-274P-ST40-US-DC5 | https://www.digikey.ca/en/products/detail/omron-electronics-inc-emc-div/G6AK-274P-ST40-US-DC5/1815812?utm_source=chatgpt.com $9.86 / piece.
4x8 Transistor ULN2803A | https://www.st.com/resource/en/datasheet/uln2801a.pdf Spec sheet https://www.digikey.ca/en/products/detail/stmicroelectronics/ULN2803A/599591?gclsrc=aw.ds&gad_source=1&gad_campaignid=23210334209&gbraid=0AAAAADrbLliTyR6dB5PNOcH-pJMFbRCXA&gclid=Cj0KCQjwgr_NBhDFARIsAHiUWr4m8lqpMY8bVF92Evks8tehyltINY4Yhkcj96YM7KdGKZq3xNLO2KgaAmPmEALw_wcB Purchase $2.71 / piece
Wall adapter WSU050-2000 | https://www.digikey.ca/en/products/detail/triad-magnetics/WSU050-2000-R/3094952 $17.54 / piece
Barrel Jack RAPC722X | https://www.digikey.ca/en/products/detail/switchcraft-inc/RAPC722X/804747 $3.03 / piece
Arduino 32-DIG | Unknown yet. Need a 32- channel Arduino/Microcontroller.

## Slide 3: Wiring:
Wiring guide:
The Arduino is connected directly to the laptop, acting as the 5V supply. The Arduino digital inputs 1 and 2 will be wired to the ULN2803A transistor boards, allowing for digital control via acquisition computer. The transistor will be powered via wall mount, with both the 5V input and GND connected to the wall power. The wall adapter will connect to a barrel jack soldered to the PCB. Two rails, one for 5V and one for GND , will be connected to the barrel jack. The transistors will connect to the relay pins of the 16 DPDT relays, with the relays powered via the 5V rail. The relays will receive input from the KOD3005P PSUs, and act as a bridge between our power supplies and current set up. The output of the relays will connect to the current configuration (resistors to coils). A PCB will be designed to automate the wiring process.